## Slide 1: Lab 2 Content
Master the connection between 8086 and 8255
  I/O Address decoding
Master the control word of 8255
Use the 8255 in mode 0
  As the input to read from 8 switches
  As the output to turn on/off 7-segment LEDs
Master the memory address mapping
  How to assign addresses to a memory chip
Understand the concept of even/odd address, high/low byte of data bus, and even/odd banks

## Slide 3: For the 8255
Determine the port number according to the circuits
Determine the control word given the requirement of each port (A/B/C) in 8255
  As the input to read from 8 switches
  As the output to turn on/off 7-segment LEDs

## Slide 4: 1) Determine the port number
Quiz：how to derive those port numbers?

## Slide 5: 2) Determine the control word
Quiz: what is the port A/B/C used for?

## Slide 6: 2) Determine the control word
Quiz: the example code configures A/B/C port as output; do we need to modify this?

## Slide 7: How to drive the 7-segment LEDs
Quiz: what’s the purpose of the above table? Is there any mistakes in it?

## Slide 8: How to drive the 7-segment LEDs
Quiz1: what would happen if we comment the “CALL DELAY” instruction in the code?
Quiz2: what would happen if we change the value of DelayShort variable?

## Slide 9: Programming Requirement
1) 8255 part

## Slide 10: Programming Requirement
1) 8255 part
Read the switch status
Turn on/off 7 segment LEDs correspondingly
Turn on/off the four colorful LEDs

## Slide 11: Programming Requirement
2) memory module part
  How to determine the memory range for each chip
  How to decide even/odd banks
  How to write to the given address range

## Slide 12: Memory Module Design
Quiz: how to decide the memory address range of U10 and U11? How to decide the segment address for data segment?

## Slide 13
Quiz：
What is the address in the U10？
【the even or odd address in xxxxH-xxxxH (64KB) 】
What about U11?

## Slide 14: The Error in the Example Code
MOV BYTE PTR [BX],0FFH
MOV [BX],0FFH
Quiz: if we want to write a byte to the address, which instruction is correct and why?
  How does the assembler know the size of memory access?

## Slide 15: Programming Requirement
Simple loop that we have done before!